## Slide 1: Chapter 1
1.1 Introduction to digital signals and systems, Properties
and operations on digital signals.
1.2 Classification of signals, system, LTI system
1.3 Convolution in time domain (linear & circular),
Correlation.
Self-Learning Topic: Correlation (Circular)

## Slide 3: Signal
A signal is a pattern of variation that carry information.
Signals are represented mathematically as a function of one or more independent variable.
A picture is brightness as a function of two spatial variables, x and y.
In this course signals involving a single independent variable, generally refer to as a time, t are considered. Although it may not represent time in specific application.
A signal is a real-valued or scalar-valued function of an independent variable t.

## Slide 4: Example of signals
Electrical signals like voltages, current and EM field in circuit
Acoustic signals like audio or speech signals (analog or digital)
Video signals like intensity variation in an image
Biological signal like sequence of bases in gene
Noise which will be treated as unwanted signal

## Slide 5
Classification of Signal
  Continuous-time and discrete-time signal
  Analog and digital signal (time and amplitude)
(1) Continuous-time signal：
(2) Discrete-time signal：Discrete variableContinuous amplitude
Time-domain discrete signals
(3) Analog Signal: Continuous variableContinuous amplitude
Speech, Television, Time-domain continuous signals
(4) Digital Signal：Discrete variablesDiscrete amplitude
Quantized discrete-time signals

## Slide 6
Signal Processing
Computer, Semiconduct and Information Science
1960’s-1970’s
Representation, transformation and manipulation
of signals and the information they contain.
Signal operation include:
(1) Transform, filter, inspection, spectrum analysis;
(2) Modulation and coding;
(3) Analog Signal Processing;
(4) Digital Signal Processing.

## Slide 7
Processing of analog signal with digital methods
(1) Digitalized process for analog signals
Sample
Quantizer
Coder
xa(t)
x(n)
(2) Digital processing method
A/D
DSP
D/A
xa(t)
ya(t)
Filter
x(n)
y(n)
Filter

## Slide 8
Feature of Digital System
(1) High accuracy: Floating point-8,16,32,64 bits
(2) High reliability: VLSI (analog: drift, calibration)
(3) Flexible: DSP, Software, FPGA, VHDL
(4) Easy to integrate
(5) Deal with high dimensional signals
(6) Low costs: reusable, reconfigurable
Advantages
(7) Data logging
(8) Adaptive capability

## Slide 9
(3) Noise process  Digital filter
(1) Selective of A/D  Signal representation - Sampling
(2) Manipulation and transform  feature extraction and analysis
Objective of Digital Signal Processing
Digital Signals
Manipulation
Digital filter
Measurement
Digital Signals
Spectrum analysis
Frequency division
Disturbance attenuation

## Slide 10: Energy and Power
Signals corrupted by noise.
Energy and Power Spectrum useful to identify signal from noise.
Energy and Power spectrum can be calculated by using Fourier transform.

## Slide 11: Power and Energy in a Physical System
The instantaneous power
The total energy
The average power

## Slide 12: Power and Energy
By definition, the total energy over the time interval in a continuous-time signal is:
denote the magnitude of the (possibly complex) number
The time average power
By definition, the total energy over the time interval in a discrete-time signal is:
The time average power

## Slide 14
Discrete signal is function of discrete independent variable.
n is integer value of independent variable.
Discrete time signal
Here independent variable is n along with sampling time (T).

## Slide 25: Sampling theorem
A continuous time signal can be represented in its samples and can be recovered back when sampling frequency fs is greater than or equal to the twice the highest frequency component of message signal (fm).

## Slide 26: Relationship between analog and digital signal by sampling

## Slide 28: Classification of Discrete Time Signals

## Slide 29: Deterministic and Random Signal
Signals specified by mathematical equations are deterministic signals
Eg: Ramp , Unit Step
Signals whose characteristics are random in nature are random signals
Eg: Noise

## Slide 30: Periodic and Non-periodic
A discrete time signal is said to be periodic if the signal remains the same after left and right shifting operation by (k.N) or T
Where k is constant
N is fundamental time period of the signal
Both k and N are integer values

## Slide 36
Even Signal: Discrete time signal exhibits symmetry with respect to n=0 it is even signal.
Even signal satisfies this condition

## Slide 38
Odd Signal: Discrete time signal exhibits antisymmetric with respect to n=0 it is odd signal.
Even signal satisfies this condition

## Slide 40
A discrete time signal is neither even nor odd is expressed as :

## Slide 41
Calculation of Even and Odd part of the signal:

## Slide 44
If energy of discrete time signal is finite and non zero then the signal is energy signal

## Slide 45
If power of discrete time signal is finite and non zero then the signal is power signal

## Slide 48
Causal Signal
Non Causal if defined for n<=0 or for both n>0 and n<=0
If system is non causal then:

## Slide 49
Non causal discrete time signal only defined for n<=0 is called anti causal signal.

## Slide 53
Downsampling = signal x(n) here n is replaced by Dn where D is an integer..
Upsampling = signal x(n) here n is replaced by n/I where I is an integer….

## Slide 58: Time Shifting of Discrete Time Signals
X(n) signal will be shifted by variable m i.e. x(n)=x(n-m)
m is positive integer signal is delayed by m units of time.
Delay results in shifting each sample of x(n) to right.
m is negative integer signal is advanced by m units of time.
Advance results in shifting each sample of x(n) to left.

## Slide 60
Addition of two discrete signals is performed on sample by sample basis.

## Slide 62
Multiplication of two discrete signals is performed on sample by sample basis.

## Slide 64: Discrete Time System
Discrete time system is device or algorithm which accepts input in discrete signal form to produce output or response in discrete time signal form.

## Slide 65: Discrete Time System

## Slide 66: LTI (Linear Time Invariant) System
A discrete time system is linear if it obeys principle of superposition and time invariant if input output relationship does not change with time.
When system satisfies property of linearity and time invariance it is called as LTI system.

## Slide 67
Basic elements of Representation are:
Adder
Constant Multiplier – Constant scaling factor
Unit Delay Element – one sample unit to delay
Unit Advance Element - one sample unit to advance

## Slide 72
Static System – Output depends on only current input samples but not on past or future samples – no memory
Dynamic System – Opposite of static

## Slide 75: Time Invariant and Time Variant System
A system is said to be time invariant if its input output characteristics do not change with time.

## Slide 76: Procedure to test for time Invariance

## Slide 77: Procedure to test for time Invariance

## Slide 78: Procedure to test for time Invariance

## Slide 82: Linear and Non Linear System
Linear system satisfies superposition principle.
Response of system to weighted sum = weighted sum of responses of the system to each individual signals

## Slide 83: Linear and Non Linear System(Check for Linearity)

## Slide 88: Causal and Non Causal Systems

## Slide 89: Causal and Non Causal Systems

## Slide 90: Causal and Non Causal Systems

## Slide 91: Causal and Non Causal Systems

## Slide 92: Stable and Unstable

## Slide 93: Stable and Unstable

## Slide 94: Stable and Unstable

## Slide 95: FIR and IIR Systems
FIR system (Finite duration Impulse Response System) , the impulse response consists of finite number of samples.
IIR system (Infinite duration Impulse Response System) , the impulse response consists of infinite number of samples.

## Slide 97: Discrete or Linear Convolution

## Slide 98: Discrete or Linear Convolution
In linear convolution the x1 and x2 sequences are non periodic , hence convolution result x3 is also non periodic.
Linear convolution is said to be aperiodic.

## Slide 102
Number of Samples in output=N1+N2-1
N1 is number of samples in x(n)
N2 is number of samples in h(n)
Here 4+4-1= 7 samples for y(n)

## Slide 104: Graphical Method

## Slide 117: Circular Convolution

## Slide 118: Circular Convolution

## Slide 136: Correlation
Used when two signals are to be compared.
Measure of degree to which two signals are similar.
Cross Correlation – correlation of two separate signals
Auto Correlation – correlation of signal with itself.

## Slide 137: Cross Correlation

## Slide 138: Auto Correlation

## Slide 144: Matrix Method for Calculating Auto and Cross Correlation.
Steps for Matrix Method Correlation
Take signal x(n) as it is.
Fold sequence y(n) to obtain y(-n).
Obtain convolution of x(n) and y(-n).
The result of convolution will be same as correlation.