## Slide 1: Chapter 3
Image Transform: Frequency Domain Representation and Enhancement 10 CO3
3.1 Introduction , DFT and its properties, radix-2 algorithm(2- DFT ), FFT algorithm: divide and conquer approach, Dissemination in Time(DIT)-FFT
3.2 Discrete Cosine Transform, Walsh Transform, Hadamard Transform, Haar Transform, Principal component Analysis(PCA/Hoteling Transform), Introduction to Wavelet Transform
3.3 Low Pass and High Pass Frequency domain filters: Ideal, Butterworth,
Homomorphic filter
Self-Learning Topic: Discrete Sine Transform (DST)

## Slide 2: Discrete Fourier Transform
Discrete fourier transform for a finite sequence is given by:
Evaluating summation for finite sequence for 0 to N-1.
k/N corresponds to frequency F
N corresponds to time for discrete signals

## Slide 3: Discrete Fourier Transform
Magnitude function
X(k) = √Xr^2(k)+Xi^2(k)
Phase function
Angle X(k)=tan-1[Xi(k)/Xr(k)]

## Slide 4: Inverse Discrete Fourier Transform

## Slide 5: Properties of DFT

## Slide 6: Properties of DFT
DFT of circular convolution of two sequences is equivalent to product of their individual DFTs.

## Slide 7: Properties of DFT
DFT of product of two discrete time sequences is equivalent to circular convolution of DFTs of individual sequences scaled by factor of 1/N.

## Slide 8: Properties of DFT
Reversing the N point sequence in time is equivalent to reversing the DFT sequence.

## Slide 9: Properties of DFT
The circular time shift property of DFT says that if discrete time signal is circularly shifted in time by m units , then its DFT is multiplied by e^-j2pikm/N

## Slide 10: Properties of DFT
Conjugation
DFT of complex conjugate of any sequence is equal to complex conjugate of DFT of that sequence , with sequence delayed by k samples in frequency domain.
DFT{x(n)}=X(k)
DFT{X*(n)}=X*(N-k)

## Slide 11: Fast Fourier Transform
FFT is method of computing DFT with reduced number of calculations.
Computational efficiency is achieved if we adopt a divide and conquer approach.
Approach is based on decomposition of N point DFT into successively smaller DFTs.

## Slide 12: Radix-2 FFT
N=2^m
m is number of stages
N point sequence is decimated into 2 point , further from a 2 point sequence 4 point DFT can be computed and so on.

## Slide 13: Phase or Twiddle Factor
Complex valued factor in DFT is defined as WN
also called as twiddle factor.
Twiddle factor is given as
W = e^(-j2*pi)
Twiddle factor can be multiplied or divided by any integer.

## Slide 14: DIT-FFT
Steps to find DFT using Radix 2 DIT FFT:

## Slide 19: Image Transforms
Image transforms are extensively used in image processing and image analysis.
Transform is basically a mathematical tool, which allows us to move from one domain to another domain (time domain to the frequency domain).
migrate from one domain to another domain is to perform the task at hand in an easier manner.

## Slide 20: Image Transforms
Image transforms are useful for fast computation of convolution and correlation.
The transforms do not change the information content present in the signal.
Transforms play a significant role in various image-processing applications such as image analysis, image enhancement, image filtering and image compression.

## Slide 21: NEED FOR TRANSFORM
Mathematical Convenience

## Slide 22: NEED FOR TRANSFORM

## Slide 24: Image Transform
1) Orthogonal sinusoidal basis function
One of the most powerful transforms with orthogonal sinusoidal basis function is the Fourier transform.
The transform which is widely used in the field of image compression is discrete cosine transform.

## Slide 25: Image Transform
2) Non-sinusoidal orthogonal basis function
The transforms whose basis functions are non-sinusoidal in nature.
One of the important advantages of wavelet transform is that signals (images) can be represented in different resolutions.

## Slide 26: Image Transform
3) Basis function depending on statistics of input signal
The transform whose basis function depends on the statistics of input signal are KL transform and singular value decomposition.
The KL transform is considered to be the best among all linear transforms with respect to energy compaction.

## Slide 27: Image Transform
4) Directional transformation
The transforms whose basis functions are effective in representing the directional information of a signal include Hough transform, Radon transform, Ridgelet transform and Contourlet transform.

## Slide 28: Need for transform
The need for transform is most of the signals or images are time domain signal (ie) signals can be measured with a function of time.
This representation is not always best.
For most image processing applications anyone of the mathematical transformation are applied to the signal or images to obtain further information from that signal.

## Slide 30: Orthogonal DFT
If A is unitary and has only real elements , then it is orthogonal matrix
A is orthogonal if A.A’ = I

## Slide 31: Image Transform
1) Check whether the DFT matrix is unitary or not.

## Slide 36: Unitary Transform
unitary transformation preserves the signal energy
Most unitary transforms pack a large fraction of the energy of the image into relatively few of the transform coefficients.
Few of the transform coefficients have significant values and these are the coefficients that are close to the origin

## Slide 37: DFT of Image Matrix (2D)

## Slide 38: DFT of Image Matrix (2D)

## Slide 42: Discrete Cosine Transform (DCT)
The discrete cosine transforms are the members of a family of real-valued discrete sinusoidal unitary transforms.
A discrete cosine transform consists of a set of basis vectors that are sampled cosine functions.
DCT is a technique for converting a signal into elementary frequency components and it is widely used in image compression.

## Slide 50: IDCT

## Slide 51: Symmetric and Asymmetric
Transformation Matrix – T
Image Matrix – f
If Transformation matrix is symmetric:
F = TfT
If Transformation matrix is asymmetric:
F = TfT’

## Slide 52: Hadamard Transform

## Slide 54: Hadamard Transform
Hadamard of Sequence
X[n]={H(N).x(n)}
Inverse Hadamard of Sequence
X[n] = 1/N{H(N).x(n)}
Hadamard of image (2D)
Hadamard is symmetric transform
F = TfT

## Slide 56: Walsh Transform

## Slide 57: Haar Transform

## Slide 58: Haar Transform

## Slide 59: IMAGE ENHANCEMENT IN THE FREQUENCY DOMAIN
If we multiply each element of the Fourier coefficient by a suitably chosen weighting function then we can accentuate certain frequency components and attenuate others.
This selective enhancement or suppression of frequency components is termed Fourier filtering or frequency domain filtering.
The spatial representation of image data describes the adjacency relationship between the pixels.
On the other hand, the frequency domain representation clusters the image data according to their frequency distribution.
In frequency domain filtering, the image data is dissected into various spectral bands, where each band depicts a specific range of details within the image.
The process of selective frequency inclusion or exclusion is termed frequency domain filtering.
It is possible to perform filtering in the frequency domain by specifying the frequencies that should be kept and the frequencies that should be discarded.

## Slide 60: IMAGE ENHANCEMENT IN THE FREQUENCY DOMAIN
f(m,n) – original image
F(k,l) – FT of original image
h(m,n) – Filtering mask
H(k,l) – FT of filtering mask

## Slide 61: Low-pass (LP) filtering
Preserves low frequencies, attenuates high frequencies.
ideal
in practice
D0: cut-off frequency

## Slide 62: Lowpass (LP) filtering (cont’d)
In 2D, the cutoff frequencies lie on a circle.

## Slide 63: Low-pass (LP) filtering
D0 is the cut-off frequency of the low-pass filter.
The cut-off frequency determines the amount of frequency components passed by the filter.
The smaller the value of D0 , the greater the number of image components eliminated by the filter.
The value of D0 is chosen in such a way that the components of interest are passed through.

## Slide 64: How does D0 control smoothing? (cont’d)
D0 controls the amount of blurring
r=8 (90%)
r=78 (99%)

## Slide 65: Ringing Effect
Sharp cutoff frequencies produce an overshoot of image features whose frequency is close to the cutoff frequencies (ringing effect).
h=f*g

## Slide 66: Low Pass (LP) Filters
Ideal low-pass filter (ILPF)
Butterworth low-pass filter (BLPF)
Gaussian low-pass filter (GLPF)

## Slide 68: Butterworth LP filter (BLPF)
In practice, we use filters that attenuate high frequencies smoothly (e.g., Butterworth LP filter)  less ringing effect
n=1
n=4
n=16

## Slide 69: Spatial Representation of BLPFs
n=1 n=2 n=5 n=20

## Slide 70: Comparison: Ideal LP and BLPF
ILPF
BLPF
D0=10, 30,
60, 160,
460
n=2
D0=10, 30,
60, 160,
460

## Slide 71: Gaussian LP filter (GLPF)
Notes: 71

## Slide 72
Example: smoothing by GLPF (1)

## Slide 73
Examples of smoothing by GLPF (2)
D0=100
D0=80

## Slide 74: High-Pass filtering
A high-pass filter can be obtained from a low-pass filter using:
= 1 -
D0

## Slide 75: High-pass filtering (cont’d)
Preserves high frequencies, attenuates low frequencies.

## Slide 76: Butterworth high pass filter (BHPF)
In practice, we use filters that attenuate low frequencies smoothly (e.g., Butterworth HP filter)  less ringing effect

## Slide 77: Comparison: IHPF and BHPF
IHPF
BHPF
D0=30,60,160
n=2
D0=30,60,160

## Slide 78: Gaussian HP filter
GHPF
BHPF

## Slide 79: Comparison: BHPF and GHPF
GHPF
BHPF
D0=30,60,160
n=2
D0=30,60,160

## Slide 80: Homomorphic filtering
Many times, we want to remove shading effects from an image (i.e., due to uneven illumination)
  Enhance high frequencies
  Attenuate low frequencies but preserve fine detail.

## Slide 81: Homomorphic Filtering (cont’d)
Consider the following model of image formation:
In general, the illumination component i(x,y) varies slowly and affects low frequencies mostly.
In general, the reflection component r(x,y) varies faster and affects high frequencies mostly.
i(x,y): illumination
r(x,y): reflection
IDEA: separate low frequencies due to i(x,y)
from high frequencies due to r(x,y)

## Slide 82: How are frequencies mixed together?
When applying filtering, it is difficult to handle
low/high frequencies separately.
Low and high frequencies from i(x,y) and r(x,y)
are mixed together.

## Slide 83: Can we separate them?
Idea:
Take the ln( ) of

## Slide 84: Steps of Homomorphic Filtering
(1) Take
(2) Apply FT:
or
(3) Apply H(u,v)

## Slide 85: Steps of Homomorphic Filtering (cont’d)
(4) Take Inverse FT:
or
(5) Take exp( ) or

## Slide 86: Example using high-frequency emphasis
Attenuate the contribution made by illumination and amplify the contribution made by reflectance
Attenuate the contribution made by illumination and amplify the contribution made by reflectance

## Slide 87: Homomorphic Filtering: Example

## Slide 88: Homomorphic Filtering: Example

## Slide 89: Karhren Loeve Transform (Hotelling Transfrom)
Also called as Eigen Vector Transform.
Based on statistical properties of image and has several important properties that make it useful for image processing – image compression.
Data from neighbouring pixels is highly correlated , so achieving image compression without losing the quality of image is a challenge.

## Slide 90: Karhren Loeve Transform (Hotelling Transfrom)
By de-correlating this data more compression can be achieved.
KL transform de-correlates the data which facilitates high degrees of compression

## Slide 91: Steps to compute KL transform

## Slide 96: Eigen Value